SHORT-FIELD TAKEOFF AND MAXIMUM PERFORMANCE CLIMB

Lesson Plan

REFERENCE:

- FAA-H-8083-3

- FAA-H-8083-23

- POH/AFM

OBJECTIVE:

To determine that the applicant:

- Exhibits knowledge of the elements related to short-field takeoff and maximum performance climb.

- Positions the flight controls for the existing wind conditions; sets the flaps as recommended.

- Clears the area; taxies into takeoff position utilizing maximum available takeoff area and aligns the airplane on the runway center / takeoff path.

- Applies brakes, while advancing the throttle smoothly to takeoff power.

- Lifts off at the recommended airspeed, and accelerates to the recommended obstacle clearance airspeed or VX.

- Establishes a pitch attitude that will maintain the recommended obstacle clearance airspeed, or VX +10/-5 knots, until the obstacle is cleared, or until the airplane is 50 feet above the surface.

- After clearing the obstacle, establishes the pitch attitude for VY, accelerates to VY, and maintains VY +10/-5 knots, during the climb.

- Retracts the landing gear, if appropriate, and flaps after clear of any obstacles or as recommended by the manufacturer.

- Maintains takeoff power and VY +10/-5 knots to a safe maneuvering altitude.

- Maintains directional control and proper wind-drift correction throughout the takeoff and climb.

- Completes the appropriate checklist.

ELEMENTS/SCHEDULE:

- POH power, flap settings, Vx and Vy speeds			(10 min)

- POH Short-field take off checklist				(10 min)

- POH Climb checklist						(10 min)

- Emergency engine out procedure				(10 min)

Total	(40 min)

INSTRUCTORS ACTIONS:

- Discuss objective

- Coach student through procedure

- Evaluate student through questioning

STUDENTS ACTIONS:

- Student to perform mock procedure in classroom

- Ask/answer questions

Completion Standards:

1. Touchdown down at or 200 ft beyond intended touchdown point with minimum float and no appreciable drift with the aircraft's longitudinal axis aligned with the runway

2. Airspeed ±5 Kts.

Common Errors:

1. Poor airspeed control

2. Uncorrected drift

3. Improper runway alignment

4. Misjudging aircraft float resulting in a long landing

Vx and Vy

Short field Takeoff